FreeEMS Tuning Tool Interface Overview

Built from several parts :

Textual definition document – core

Textual definition document – firmware specific

Structure types

Interface version (4 parts)

Primitives
key, length (bits or bytes?), name
UnsignedChar, 1, Integer Unsigned Char
UnsignedShort, 2, Integer Unsigned Short
UnsignedLong, 4, Integer Unsigned Long
SignedChar, 1, Integer Signed Char
SignedShort, 2, Integer Signed Short
SignedLong, 4, Integer Signed Long
Boolean, 0.125, Boolean
Character, 1, Character

Structures
key, name, size in bytes, structure definition
maintable, Main Table, 1024, {etc}
twodtableUS, 2D Table US, 64, {etc}
fixedconfig1, Fixed Configuration Data One, 1024, {etc}

structure def = list of components in order

component = prim key, translation offset, translation factor, unit, name, description, count

Packet types

Interface version

list of packets
each :
key
name
description
payload ID
request structure
reply structure

Block / location definitions

Interface version

list of blocks
each :
key
name
description
block ID
list of payload id types
list of components each of which can be a block or a structure or a primitive

Additionally, an application implementing this should :
store the settings in the standard semi raw settings format (and optionally others also)
output datalogs in the standard plain text datalog format too (and optionally others also)